## Slide 1: ICP Design proposal

## Slide 2
Deployer (Power8-LC or x86)
10 Gb
1 Gb
LC922
High Level Network Architecture Diagram – Cloud Native
Per Server Node
2x10G DAC Cables
2x 1G Cat5e Cables
2x10G
2x1G
Data
Customer Up-Links
LC922
Data
OS provisioning
IPMI
OS provisioning
IPMI

## Slide 3: Racking / Configuration
Rack:
QTY: 1
SlimRack 7965-94Y
PDUs
Network:
1 x Lenovo G8264CS (10G data network)
1*x Lenovo G8052 (1G management network)
Worker Building Block:
QTY: 2
Server Config:
LC922
Processor – POWER9 20 Cores ( 2.7Ghz)
Memory - 512GB ,
2 x 128 GB SATA DOMs (boot/OS)
8 x 480 GB SSDs (storage pool)
Built-in 10G ethernet
Deployment Node (POWER8– LC Option ):
QTY: 1
Habanero S812LC(8348-21C) tested
Should support any POWER8/9-LC system
Deployment Node (x86 option):
QTY: 1
Server Config:
Lenovo M4
Processor - 2 Cores
Memory – 32GB
1 x 1 TB Sata HDDs
2 x 2-Port 10G NIC ( Intel 10G/Mellanox)
Control Plane Building Block:
QTY: 3
Server Config:
LC922
Processor – POWER9 20 Cores ( 2.7Ghz)
Memory - 512GB ,
2 x 128 GB SATA DOMs (boot/OS)
8 x 480 GB SSDs (storage pool)
Built-in 10G ethernet

## Slide 4
Deployer (Power8-LC or x86)
10 Gb
1 Gb
AC922
High Level Network Architecture Diagram – Cognitive Computing
Per Server Node
2x10G DAC Cables
2x 1G Cat5e Cables
2x10G
2x1G
OS provisioning
IPMI
Data
Customer Up-Links
LC922
OS provisioning
IPMI
Data

## Slide 5: Racking / Configuration
Rack:
QTY: 1
SlimRack 7965-94Y
PDUs
Network:
1 x Lenovo G8264CS (10G data network)
1*x Lenovo G8052 (1G management network)
Worker Building Block:
QTY: 2
Server Config:
AC922
Processor – POWER9 22 Cores ( 2.8Ghz)
GPU – 4 x Nvidia Tesla V100 (air cooled)
Memory - 512GB
2 x 1.92TB SSDs
2 x PCIe2 10GbE SFP+ CU 4-port converged network adapter
Deployment Node (POWER8 – LC Option ):
QTY: 1
Habanero S812LC(8348-21C) tested
Should support any POWER8/9-LC system
Deployment Node (x86 option):
QTY: 1
Server Config:
Lenovo M4
Processor - 2 Cores
Memory – 32GB
1 x 1 TB Sata HDDs
2 x 2-Port 10G NIC ( Intel 10G/Mellanox)
Control Plane Building Block:
QTY: 3
Server Config:
LC922
Processor – POWER9 20 Cores ( 2.7Ghz)
Memory - 512GB ,
2 x 128 GB SATA DOMs (boot/OS)
8 x 480 GB SSDs (storage pool)
Built-in 10G ethernet